## Slide 1: Chapter 3
PIC18F Programming Model and Its Instruction Set
Updated: 2/10/2019

## Slide 3: Data Memory
Decoded Instruction
from Program
Memory:
Arithmetic/Logic Function to be Performed
Result Destination
Address of Second Source Operand
Opcode
d a Address
a-bit
a = 0 access bank a = 1 use BSR
Organization
000h
07Fh
080h
0FFh
100h
1FFh
200h
2FFh
D00h
DFFh
E00h
EFFh
F00h F7Fh
F80h FFFh
Instruction Examples:
MOVLW MOVWF
0x23
0xF3
MOVWF MOVWF
0xF2
0x200
4k bytes Data Memory

## Slide 4: Data Memory
Decoded Instruction
from Program
Memory:
Arithmetic/Logic Function to be Performed
Result Destination
Address of Second Source Operand
Opcode
d a Address
a-bit
a = 0 access bank a = 1 use BSR
Organization
000h
07Fh
080h
0FFh
100h
1FFh
200h
2FFh
D00h
DFFh
E00h
EFFh
F00h F7Fh
F80h FFFh
Instruction Examples:
MOVLW MOVWF
0x23
0xF3
MOVWF MOVWF
0xF2
0x200
0x200 Does not fit in Operand Field; 0x200 is large than ACCESS Bank
4k bytes Data Memory

## Slide 5: Data Memory
BSR
Organization
Access RAM
Bank 0 GPR
Bank 2 GPR
Bank 13 GPR
Bank 14 GPR
Bank 15 GPR
Access SFR
000h
07Fh
080h
0FFh
100h
Bank 1 GPR
1FFh
200h
2FFh
D00h
DFFh
E00h
EFFh
F00h F7Fh
F80h FFFh
4k bytes Data Memory
0 x 2 00
Opcode
d a Address
8 bit operand

## Slide 6: Data Memory
Decoded Instruction
from Program
Memory:
Arithmetic/Logic Function to be Performed
Result Destination
Address of Second Source Operand
Opcode
d a Address
a-bit
a = 0 access bank a = 1 use BSR
Organization
Instruction Examples:
MOVLW MOVWF
0x23
0xF3
MOVWF MOLB MOVWF
0xF2
0x02
0x20,1
Access RAM
Bank 0 GPR
Bank 1 GPR
Bank 2 GPR
Bank 13 GPR
Bank 14 GPR
Bank 15 GPR
Access SFR
000h
07Fh
080h
0FFh
100h
1FFh
200h
2FFh
D00h
DFFh
E00h
EFFh
F00h F7Fh
F80h FFFh
4k bytes Data Memory
Loading BSR

## Slide 7: Data Memory
Access RAM
Organization
PIC16F8F2520/4520
Register File Map
256 Bytes
Bank 0 GPR
Bank 1 GPR
Bank 2 GPR
Bank 13 GPR
Bank 14 GPR
Bank 15 GPR
Access SFR
Access RAM
Access SFR
000h
07Fh
080h
0FFh
100h
1FFh
200h
2FFh
D00h
DFFh
E00h
EFFh
F00h F7Fh
F80h FFFh
00h
7Fh
80h FFh
Data Memory up to 4k bytes
Divided into 256 byte banks
Half of bank 0 and half of bank 15 form a virtual bank
that is accessible no matter which bank is selected
Remember:
Virtual bank:
Access Bank
4k bytes Data Memory

## Slide 8: Register File Concept
Data Bus
d
Decoded Instruction
from Program
Memory:
Arithmetic/Logic Function to be Performed
Result Destination
Address of Second Source Operand

memory location
w
f
w
f
ALU
WREG
Data Memory (Register File)
07h  Register File Concept: All of data memory is part of the register file, so any location in data memory may be operated on directly
All peripherals are mapped into data memory as a series of registers
 Orthogonal Instruction Set: ALL instructions can operate on ANY data
08h
09h
0Ah
0Bh
0Ch
0Dh
0Eh
0Fh
10h
Opcode
d a Address
0 1
a-bit
a = 0 access bank a = 1 use BSR

## Slide 9: PIC18F Programming Model (1 of 2)
The representation of the internal architecture of a microprocessor, necessary to write assembly language programs
  Programming Model
Two Groups of Registers in PIC16 8-bit Programming Model (all in SRAM)
  ALU Arithmetic Logic Unit (ALU)
  Special Function Registers (SFRs)

## Slide 10: PIC18F Programming Model (2 of 2)
Register Size: 16
Register Size: 8
Two Groups of Registers in PIC16 8-bit Programming Model
Register Size: 8

## Slide 11: Registers
WREG
  8-bit Working Register (equivalent to an accumulator)
  Used for arithmetic and logic operations
BSR: Bank Select Register (0 to F)
  4-bit Register
 Only low-order four bits are used to provide MSB four bits of a12-bit address of data memory.

## Slide 12: Register Direct Addressing
BSR (Bank Select Register) 4-bits from BSR Register
'f’ Operand
8-bits Encoded in Instruction
0 0 1 0 1 0 0 0 0 0 1 0
0x282
12-bit Effective Address (Use this when coding)
00
01
02
03
7D
7E
7F
80
81
82
FC FD FE FF
Bank1
Bank2
Bank13
Bank14
Bank15
'a’ Bit from Instruction
a bit = 1
Bank0

## Slide 13: Register Direct Addressing
BSR (Bank Select Register) 4-bits from BSR Register
'f’ Operand
8-bits Encoded in Instruction
0 0 1 0 1 0 0 0 0 0 1 0
0x082
12-bit Effective Address (Use this when coding)
00
01
02
03
7D
7E
7F
80
81
82
FC FD FE FF
Bank1
Bank2
Bank13
Bank14
Bank15
'a’ Bit from Instruction
a bit = 0
Bank0

## Slide 14: Register Direct Addressing
BSR (Bank Select Register) 4-bits from BSR Register
'f’ Operand
8-bits Encoded in Instruction
0 0 0 0 1 0 0 0 0 0 1 0
0x082
12-bit Effective Address (Use this when coding)
00
01
02
03
7D
7E
7F
80
81
82
FC FD FE FF
Bank1
Bank2
Bank13
Bank14
Bank15
'a’ Bit from Instruction
a bit = 1
Bank0

## Slide 15: STATUS: Flag Register Flags in Status Register
Remember:
NOVember iZ Damn Cold in Canada
C (Carry/Borrow Flag): set when an addition generates a carry and a subtraction generates a borrow
DC (Digit Carry Flag): also called Half Carry flag; set when carry generated from Bit3 to Bit4 in an arithmetic operation
  Used for BCD representation
Z (Zero Flag): set when result of an operation is zero
OV (Overflow Flag): set when result of an operation of signed numbers goes beyond seven bits – if the results fall outside 127 (0x7F) and -128 (0x80)
N (Negative Flag): set when bit B7 is one

## Slide 16: Example:
PIC18 Visual Interpreter
ADD: WREG=9F and L=72. Which flags will be set?
1001 1111 N=0
0111 0010 OV=0 // not signed numbers
------------- Z=0 0001 0001 DC=1
=0x11 C= 1
0111 0010
1001 1111
------------- 0001 0001
=0x11
1
WREG=9F

## Slide 17: Example:
PIC18 Visual Interpreter
ADD: WREG=9F and L=72. Which flags will be set?
1001 1111 N=0
0111 0010 OV=0 // not signed numbers
------------- Z=0 0001 0001 DC=1
=0x11 C= 1
0111 0010
1001 1111
------------- 0001 0001
=0x11
1
WREG=0x11
The results will be directed back to WREG since d=0 Note that for ADDLW instruction the d bit is always ZERO!

## Slide 18: Example:
PIC18 Visual Interpreter
ADD: Literal=0x9F and WREG=0x52. Which flags will be set?
N=1 OV=0 Z=0 DC=1 C=0
1
1001 1111
0101 0010
------------- 1111 0001
= 0xF1
WREG=0x52
0x9F
0xF1

## Slide 19: Examples
Clearing STATUS Register
L-WW
L-WW
Note: 0x01-0x8081/ Note that this can be interpreted as 1-(-128)=+129 Overflow!
Practice These Instructions!!
DC,N,OV
DC,C,OV

## Slide 20: How OV Is Calculated
 Read this for a very good description as to how OV works:

http://teaching.idallen.com/dat2343/10f/notes/040_overflow.txt
 We compare carry into 7th bit and carry out of the 7th bit; if they are EQUAL then no overflow, else there is an overflow. Basic steps:


When ADDING just add the two numbers; THEN check Carry-IN and Carry-OUT
When SUBTRACTING (X-Y); FIRST convert Y to 2’s complement THEN calculate X+Y_2’sComp FINALLY check Carry-IN and Carry-OUT
 Try the following (assuming all numbers are in HEX):







0xFF-0x12 ; no overflow because 0xFF+0xEE Carry into bit 7=Carry out from 7th bit 0x12-0xFF ; no overflow because 0x12+0x1  Carry into bit 7=Carry out
0x80-0xFF : Carry into bit 7=Carry out  no overflow 0xFF-0x81; Carry into bit 7 = Carry out  No overflow 0xA-0x81: Carry into bit 7 NOT = Carry out  overflow 0x1-0xFA: Carry into bit 7 = Carry out  No overflow
0xEF-FB: Carry into bit 7 = Carry out from 7th bit No overflow

## Slide 21: File Select Registers (FSR)
Three registers holding 12-bit address of data registers
  FSR0, FSR1, and FSR2
File Select Registers composed of two 8-bit registers (FSRH and FSRL)
Used as pointers for data registers for indirect addressing
Associated with index (INDF) registers
Find FSR0-FSR2 in Special Function Register –
What are the File addresses
for each? / How many INDF do you find?

## Slide 22: File Select Registers (FSR) –
Indirect Addressing
The main application of FSR is Indirect Addressing
  FSRs will be pointing at the address of the data file and they can be incremented
  This is much easier than using direct addressing
1A
2D
3D
4D
0x1F34
FSR0=0x1F34
Data Memory
FSR0L=0x34
FSR0H=0x1F

## Slide 23: Direct and Indirect Addressing
BSF
BSF Register – Two Bytes
Remember: We are taking about DATA MEMORY!
WE WILL DISCUSS THIS IN MORE DETAILS WHEN WE LEARN MORE AOUT COMMANDS!
http://ww1.microchip.com/downloads/en/DeviceDoc/31006a.pdf

## Slide 24: Stack and Table Pointers
Table Pointer
  21-bit register used as a memory pointer to copy bytes between program memory and data registers
Stack Pointer (SP)
  Stack is a group of 31 word-size registers used for temporary storage of memory address during execution
  Used to store the return address
  Requires 5-bit address
  Saved in STKPTR in SFR
  Used primarily for saving PC for next program address prior to entering subroutine

## Slide 25
FSR
Don’t confuse SFRs and FSRs (file Select Registers)

## Slide 26: Program Counter
PCL
7 6 5 4 3 2 1 0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
PCU PCH
21 20 19 18 17 16 15 14 13 12 11 10 9 8
21-bit register functions as a pointer to program memory during program execution
PCLATH | PCLATL | PCL
Program Counter
21-bit PC can access up to 221 = 2MB (1MWord)
22nd bit used to access configuration memory at program time or via table reads & writes
Contains address of NEXT instruction (pipelining)
Lower byte accessible in data memory as PCL
Upper bytes indirectly accessible via PCLATH/PCLATU
Bit 0 of PC is always '0’ except when reading or writing program memory via table read/write mechanism
PCL

## Slide 27: 21-Bit PC Example & Program Memory
Leave space

## Slide 28: Program Memory is Byte Addressable
16-bit Program Memory
0x000003 0x000002
0x000007 0x000006
0x00000B 0x00000A
0x00000F 0x00000E
High Byte Address Low Byte Address
Low byte has even address, high byte has odd address
Addresses of instructions are always even
16-bit wide program memory is byte addressable
All program instructions will start at an even address
So if we are jumping 4 instructions ahead, we are actually jumping 8-bytes (or 8 word addresses) ahead
Word Address
0x000001 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0x000000
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
0x000005 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0x000004
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
0x000009 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0x000008
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
0x00000D 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0x00000C
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
PC

## Slide 29: Instruction Pipelining
 Instruction fetch is overlapped with execution of previously fetched
instruction
movlw 0x92
movwf REG1
MAIN movlw 0x37
movwf REG0
1
2
3
4
Example Program
Fetch
Execute
Instruction Cycles
Fetch
Execute
Fetch
Execute
Fetch
T0 | T1 | T2 | T3 | T4 | T5 | T6 | T7
Time to execute 16-bit instructions
Execute
Remember: In PIC ONE Instruction Cycle takes 4 Clock Cycle:
Clock Cycles Instruction Cycle
1 2
3
4

## Slide 30: Introduction to PIC18 Instruction Set
Includes 77 instructions;
  73 one-word (16-bit) long
  Four two-words (32-bit) long
Divided into seven groups
  Move (Data Copy) and Load
  Arithmetic
  Logic
  Program Redirection (Branch/Jump)
  Bit Manipulation
  Table Read/Write
  Machine Control
Move / Copy
Arithmetic
Logic
Branches
Bit Manipulation
Table Read/Write
Machine Control

## Slide 31
Move and Load Instructions
MOVLW
MOVLW
8-bit ;Load an 8-bit literal in WREG 0 x F2
 MOVWF
F, a
 MOVWF
0x25, 0
;Copy WREG in File (Data) Reg.
; If a = 0, F is in Access Bank
;If a = 1, Bank is specified by BSR
;Copy W in Data Reg.25H
 MOVFF
fs, fd
 MOVFF
0x20,0x30
;Copy from one Data Reg. to
;another Data Reg.
;Copy Data Reg. 20 into Reg.30
Move / Copy
Arithmetic
Logic
Branches
Bit Manipulation
Table Read/Write
Machine Control
L
W
Fa
Fb

## Slide 32
Arithmetic Instructions (1 of 3)
 ADDLW | 8-bit | ;Add 8-bit number to WREG
 ADDLW | 0x32 | ;Add 32H to WREG
 ADDWF | F, d, a | ;Add WREG to File (Data) Reg.
 |  | ;Save result in W if d =0
 |  | ;Save result in F if d = 1
 ADDWF | 0x20, 1 | ;Add WREG to REG20 and ;save result in REG20
 ADDWF | 0x20, 0 | ;Add WREG to REG20 and ;save result in WREG
Move / Copy
Arithmetic
Logic
Branches
Bit Manipulation
Table Read/Write
Machine Control
W
L Fa W
OR

## Slide 33: Arithmetic Instructions (2 of 3)
 ADDWFC F, d, a
;Add WREG to File Reg. with
;Carry and save result in W or F
;Subtract WREG from literal
;Subtract WREG from File Reg.
SUBLW
SUBWF
SUBWFB
8-bit F, d, a
F, d, a
INCF
DECF
COMF
NEGF
F, d, a
F, d, a
F, d, a F, a
;Take 2’s Complement-File Reg.
L-WW
;Subtract WREG from File Reg. F-WDest.
;with Borrow
;Increment File Reg.
;Decrement File Reg.
;Complement File Reg.
Fa W C

## Slide 34: Arithmetic Instructions (3 of 3)
 MULLW 8-bit ;Multiply 8-bit and WREG
 MULWF
 DAW
;Save result in PRODH-PRODL F, a ;Multiply WREG and File Reg.
;Save result in PRODH-PRODL
;Decimal adjust WREG for BCD
;Operations
0xA
Example:
MOVLW DAW
;W=A
;W=10

## Slide 35: Logic Instructions
ANDLW ANDWF | 8-bit F, d, a | ;AND literal with WREG ;AND WREG with File Reg. and ;save result in WREG/ File Reg.
 IORLW | 8-bit | ;Inclusive OR literal with WREG
 IORWF | F, d, a | ;Inclusive OR WREG with File Reg. ;and save result in WREG/File Reg.
 XORLW | 8-bit | ;Exclusive OR literal with WREG
 XORWF | F, d, a | ;Exclusive OR WREG with File Reg.
;and save result in WREG/File Reg.

## Slide 36: And, XOR, and IOR
A B T
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
( T = A ∙ B )
X X X X X X X X
AND 0 0 0 0 1 1 1 1
0 0 0 0 X X X X
Cleared to zero
XOR
X X X X
0 0 0 0
X X X X
1 1 1 1
X X X X
Toggled
X X X X X X X X
IOR
0 0 0 0 1 1 1 1
X X X X
1 1 1 1
Set to one
X X X X
If they are the same0 If they are different1

## Slide 37: Examples
MOVLW 0x1F ANDLW 0xFC
;clear bits 0 and 1
;set bits 6 and 7
Stop:
IORLW GOTO
0xC0
Stop
;invert left 3 bits
Stop:
MOVLW 0x90 XORLW 0xE0
GOTO Stop

## Slide 38: Branch Instructions
BNOV n
BC n ;Branch if C flag = 1 within + or – 64 Words
BNC n ;Branch if C flag = 0 within + or – 64 Words (NO CARRY)
BZ n ;Branch if Z flag = 1 within + or – 64 Words
BNZ n ;Branch if Z flag = 0 within + or – 64 Words
BN n ;Branch if N flag = 1 within + or – 64 Words
BNN n ;Branch if N flag = 0 within + or – 64 Words
BOV n ;Branch if OV flag = 1 within + or – 64 Words
;Branch if OV flag = 0 within + or – 64 Words
GOTO Address: Branch to 20-bit address unconditionally

## Slide 39: Branch Example
BCN 0xFA
;Brant-If-No-Carry to location:
;  PC(current_Decimal) + 2 + 2x Decimal(0xFA)
; Note 0xFA is signed!
; PC + 2 + 2(-6)
Check the table in The TEXT (p78)!
1 Word Instruction / 1 Instruction Cycle / 4 Clock Cycles

## Slide 40: Branch Instructions

## Slide 41: Call and Return Instructions
RCALL nn ;Call subroutine within +or – 512 words
CALL 20-bit, s
RETURN, s

RETFIE, s

;Call subroutine
;If s = 1, save W, STATUS, and BSR
;Return subroutine
;If s = 1, retrieve W, STATUS, and BSR
;Return from interrupt
;If s = 1, retrieve W, STATUS, and BSR
Review

## Slide 42: Bit Manipulation Instructions
 BCF | F, b, a | ;Clear bit b of file register. | b = 0 to 7
 BSF | F, b, a | ;Set bit b of file register. | b = 0 to 7
 BTG | F, b, a | ;Toggle bit b of file register. | b = 0 to 7
RLCF F, d, a
RLNCF F, d, a
RRCF F, d, a

RRNCF F, d, a
;Rotate bits left in file register through
; carry and save in W or F register
;Rotate bits left in file register
; and save in W or F register
;Rotate bits right in file register through
; carry and save in W or F register
;Rotate bits right in file register
; and save in W or F register

## Slide 43: Rotations
Rotate Right through Carry RRCF
Rotate LEFT through Carry RLCF
RLNCF
RRNCF

## Slide 44: Test and Skip Instructions
BTFSC F, b, a ;Test bit b in file register and skip the
;next instruction if bit is cleared (b =0)
BTFSS F, b, a ;Test bit b in file register and skip the
;next instruction if bit is set (b =1)
 CPFSEQ | F, a | ;Compare F with W, skip if F = W
 CPFSGT | F, a | ;Compare F with W, skip if F > W
 CPFSLT | F, a | ;Compare F with W, skip if F < W
 TSTFSZ | F, a | ;Test F; skip if F = 0

## Slide 45: Example
MOVLW | 0x1F | 
BCF | WREG, 0 | ;clear bit 0
BCF | WREG, 1 | ;clear bit 1
BSF | WREG, 6 | ;set bit 6
BSF | WREG, 7 | ;set bit 7
Stop: GOTO | Stop | 
MOVLW BTFSS | 0x7F WREG, 7 | ;load test data
BCF | WREG, 0 | ;clear bit 0
Stop: GOTO | Stop | 

## Slide 46: Increment/Decrement and Skip Next Instruction
 DECFSZ
F, d, a ;Decrement file register and skip the
;next instruction if F = 0
DECFSNZ F, d, a ;Decrement file register and skip the
;next instruction if F ≠ 0
INCFSZ F, d, a ;Increment file register and skip the
;next instruction if F = 0
INCFSNZ F, d, a ;Increment file register and skip the
;next instruction if F ≠ 0

## Slide 47: Table Read/Write Instructions (1 of 2)
 TBLRD*
 TBLRD*+
 TBLRD*-
;Read Program Memory pointed by TBLPTR
;into TABLAT
;Read Program Memory pointed by TBLPTR
;into TABLAT and increment TBLPTR
;Read Program Memory pointed by TBLPTR
;into TABLAT and decrement TBLPTR
 TBLRD+* ; Increment TBLPTR and Read Program
; Memory pointed by TBLPTR into TABLAT
Review

## Slide 48: Table Read/Write Instructions (2 of 2)
 TBLWT*
 TBLWT*+
 TBLWT*-
 TBLWT+*
;Write TABLAT into Program Memory pointed
;by TBLPTR
; Write TABLAT into Program Memory pointed
;by TBLPTR and increment TBLPTR
; Write TABLAT into Program Memory pointed
;by TBLPTR and decrement TBLPTR
; Increment TBLPTR and Write TABLAT into
; Program Memory pointed by TBLPTR
Review

## Slide 49: Machine Control Instructions
CLRWDT ;Clear Watchdog Timer
  Helps recover from software malfunction
  Uses its own free-running on-chip RC oscillator
  WDT is cleared by CLRWDT instruction
RESET ;Reset all registers and flags
  When voltage < a particular threshold, the device is held in reset
  Prevents erratic or unexpected operation
SLEEP
NOP
;Go into standby mode
;No operation

## Slide 50: Sleep Mode
Events that wake processor from sleep
MCLR
INT
TMR1
PORTB
 The processor can be put into a power-down mode by executing the SLEEP instruction




System oscillator is stopped
Processor status is maintained (static design) Watchdog timer continues to run, if enabled
Minimal supply current is drawn - mostly due to leakage (0.1 - 2.0A typical)
Master Clear Pin Asserted (pulled low)
WDT Watchdog Timer Timeout
INT Pin Interrupt
Timer 1 Interrupt (or also TMR3 on PIC18)
ADC A/D Conversion Complete Interrupt CMP Comparator Output Change Interrupt CCP Input Capture Event
PORTB Interrupt on Change
SSP Synchronous Serial Port (I2C Mode) Start / Stop Bit Detect Interrupt PSP Parallel Slave Port Read or Write

## Slide 51: Instruction Format (1 of 3)
The PIC18F instruction format divided into four groups
  Byte-Oriented operations
  Bit-Oriented operations
  Literal operations
  Branch operations

## Slide 52: PIC18 Instruction Set Overview –
0
15
Byte Oriented Operations
ADDWF
Destination
File Register Address
 |  | O | pco | de |  |  | a | f | f | f | f | f | f | f | f
9 8 7
 |  | Op | co | e |  | d |  | a |  | f | f | f | f | f | f | f | f
 |  |  |  |  |  |  |  |  | File Register Address |  |  |  |  |  |  |  | 
Or BSF
0x25, W, A
Use Access Bank (Optional)
OR
d
Destination (W or F) Access Bank

## Slide 53: Instruction Set Overview
0
9 8 7
15
Bit Oriented Operations
Bit Position (0-7)
BSF 0x25, 3, A
Access Bank (Optional)
File Register Address
11
 | Op | cod | e | b | b |  | b | a | f | f | f | f | f | f | f | f
 |  |  |  |  |  | File Register Address |  |  |  |  |  |  |  |  |  | 
Bit Position

## Slide 54: Instruction Set Overview
0
Literal and Control Operations
15 8 7 Literal Value
d
MOVLW
0x25
Literal Value
 |  |  | Op | co | e |  |  | k | k | k | k | k | k | k | k
 |  |  |  |  |  |  | Op | co | e |  |  |  |  |  | 
OR
d

## Slide 55: Instruction Set Overview
0
15
d
12 11 Source Register Address
- Two-word instruction
Byte to Byte Move Operations(2 Words)
MOVFF
0x125, 0x140
Source Address
 | Op | co | e | fs | fs | fs | fs | fs | fs | fs | fs | fs | fs | fs | fs
Opcode |  |  |  | fd fd fd fd fd fd fd fd fd fd fd fd |  |  |  |  |  |  |  |  |  |  | 
Destination Register Address
Destination Address

## Slide 56: Instruction Set Overview
0
15
Call and Goto Operations (2 Words)
CALL
0x1125
Subroutine Address
11 8 7
d
 |  |  | Op | co | e |  |  | n8 | n7 | n6 | n5 | n4 | n3 | n2 | n1
Opcode |  |  |  | n20 n19 n18 n17 n16 n15 n14 n13 n12 n11 n10 n9 |  |  |  |  |  |  |  |  |  |  | 

## Slide 57: Example (do it in class!)
ORG REG0 REG1 REG2
0x20
EQU 0x00
EQU 0x01
EQU 0x02
0x37 REG0,0 0x92 REG1,0 REG0,0 REG2, 0
MOVLW MOVWF MOVLW MOVWF ADDWF MOVWF SLEEP
Explain what this program does, specify PC value for each line, which flags are changed as the program is executed.
Command | PC | REG0,1,2 | STATUS | Time

## Slide 58: Example
ORG REG0 REG1 REG2
0x20
EQU 0x00
EQU 0x01
EQU 0x02
0x37 REG0,0 0x92 REG1,0 REG0,0 REG2, 0
MOVLW MOVWF MOVLW MOVWF ADDWF MOVWF SLEEP
W=0x37
REG0=0x37
W=0x92
REG1=0x92
W=37+92=C9
REG2=C9
NOTES:
Each 1W instruction take 4 clock periods Use the STOPWATCH in the simulator!

## Slide 59: Next QUIZ: Review the Following
Arithmetic commands (ADDLW, ADDWF, ADDWFC, SUBLW, SUBWF, SUBWB, INC, DEC, MULLW, NEGF, COMPF)
Logical commands, ANDLW, XOR, IOR, AND)
MOVE & Copy (MOVLW, MOVFF, MOVWF, CLR, SETF)
Branches (BC, BNC, BZ, BNZ, BOV, BRA, GOTO)
Bit manipulations (BCF, BSF, BTG, RLCF, RRCF)
Make sure you know about flags.
Make sure you can do the homework assignment