## Slide 1: Chapter 5
Instruction to Data Copy
2/21/14

## Slide 2: Data Copy (Move) and Set/Clear Operations
The data copy operations are classified as:
Loading 8-bit data directly in WREG
Copying data between WREG and data (file) register including I/O ports
Copying data from one data (file) register to another data (file) register
Clearing or setting all data bits in data (file) register
Exchanging low-order four bits (nibble) with high-order four bits in data (file) register

## Slide 3: Frequently Used Registers in ALU, Memory, and I/O Ports for Data Copy
Literal to W
W F
F F
F Program memory
Swapping lower order with the higher-order

## Slide 4: Addressing Modes
A way of specifying of an operand
 Direct addressing
  The operand is a part of the instruction
 Indirect addressing
  An address is specified in a register and the MPU looks up the address in that register

## Slide 5: MOV (Copy) Operations
Instructions
 MOVLW
8-bit
 MOVWF F, a
 MOVF
F,d, a
 MOVFF
Fs, Fd
Examples
 MOVLW 0xF2
Load F2H in WREG
 MOVWF REG1, 0 Copy WREG in REG1
 MOVF REG1, 1
Copy REG1 in REG1 (check for flag)
MOVF REG1, 0 Copy REG1 into WREG
MOVFF REG1,REG2 Copy REG1 into REG2
d=0 or omitted then  WREG
a=0 or omitted then  data reg is from Access Bank

## Slide 6: SET/CLR Instructions
Instructions
 CLRF F,a
 SETF F, a
 SWAP
F,d,a
Examples
CLRF REG1,0 Clear REG1 located in access bank
SETF REG1,0 Set all bits in REG1
SWAP REG1,1,0 Exchange low and high
nibbles in REG1, save in REG1

## Slide 7: Using File Select Registers (FSRs) as Pointers to Data Registers – Indirect addressing
Memory pointer is a register that holds the address of a data register
 This is called indirect addressing
 Easy to move/copy an entire block
Three registers: FSR0, FSR1, and FSR2
 Each FSR has a High and Low byte associated with an index
 Used as memory pointers to data registers
Each can be used in five different formats (operands) :
 INDF0:
 POSTINC0:
 POSTDEC0:
 PREINC0:
 PLUSW0:
Use FSR0 as pointer (index)
Use FSR0 as pointer and increment FSR0 Use FSR0 as pointer and decrement SR0 Increment FSR0 first and use as pointer Add W to FSR0 and use as pointer

## Slide 8: Indirect Addressing - Example
LFSR FSR1,120 ; LOAD 12-BIT ADDRESS 120h INTO FSR1
Initially FSR values are 0 and status of registers are given as above
LFSR
LFSR
FSR1,0x0120 ; load the FSR2,0x0150
MOVFF POSTINC1, POSTINC2
0x0 0x0
; Load the content of FSR1FSR2 and increment FSR1 & FSR2

## Slide 9: Indirect Addressing – Example (1)
Examples:
MOVFF INDF0,INDF1
ADDWF POSTINC0,1
; COPY BYTE FROM REGISTERS SHOWN BY
;FSR0 TO FSR1- NO CHANGE IN FSR
; ADD BYTE FROM REGISTERS SHOWN BY
;FSR0 AND WREG ;
;FSR0 IS INCREMENTED
Hence, we will have A3 in register 0x151 after the MOVFF instruction
Note that the pointer indexes are not changing!
A3
FSR0
FSR1

## Slide 10: Indirect Addressing Example (2)
Assume W=2; after the ADD operation, A3+2=A5Reg 0x0121, then FSR=0x0122
A5
0x0122
Examples:
MOVFF INDF0,INDF1
ADDWF POSTINC0,1
; COPY BYTE FROM REGISTERS SHOWN BY
;FSR0 TO FSR1- NO CHANGE IN FSR
; ADD BYTE FROM REGISTERS SHOWN BY
;FSR0 AND WREG ;
;FSR0 IS INCREMENTED
FSR0
FSR1
A3

## Slide 11: Initializing the RAM – Application of Indirect Addressing
What is this doing?

## Slide 12: Using Table Pointers to Copy Data
21 bit
16 bit
8-bit data registers

## Slide 13: Using Table Pointers to Copy Data from Program Memory into Table Latch (REFER TO PAGE 82-83)
TBLRD*
 Copy from Program Memory into Table Latch Using Table Pointer
TBLRD*+
 Copy from Program Memory into Table Latch and Increment Table Pointer
TBLRD*-
 Copy from Program Memory into Table Latch and Decrement Table Pointer
TBLRD+*
 Increment Table Pointer first and then copy from Program Memory into Table Latch

## Slide 14: Using Table Pointers to Copy Data from Table Latch into Program Memory
TBLWT*
 Copy from Table Latch into Program Memory Using Table Pointer
TBL WT*+
 Copy from Table Latch into Program Memory and Increment Table Pointer
TBL WT*-
 Copy from Table Latch into Program Memory and Decrement Table Pointer
TBLWT+*
 Increment Table Pointer first and then copy from Table Latch into Program Memory

## Slide 15: Copying Data from Program
Memory to Table Latch
Using TBLRD*: Address: 01251H = 76 TABLAT=76 TBLPTR=01251H
76

## Slide 16: Copying Data from Table
Latch to Program Memory

## Slide 17: Arithmetic Operations
 The PIC18F MPU performs the following arithmetic operations:
 Add
 Subtract
 Multiply
 Complement (1s and 2s)
 Increment
 Decrement

## Slide 18: Addition
Instructions:
 ADDLW
8-bit
 ADDWF
F, d, a
 ADDWFC F, d, a
Examples
 ADDLW 0xA2
Add A2H to WREG
 ADDWF REG1, 0
Add WREG to REG1 and save the sum in W
 ADDWF REG1, 1
Add WREG to REG1 and save the sum in REG1
 ADDWFC REG2, 0
Add WREG, REG2 and Carry from previous operation and save the sum in WREG
Impacts all the flags
Result can be saved in W if d=0
ADDWFC is used for numbers > 8-bit

## Slide 19: ADDWF Example
WREG + | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | (4FH)
REG20 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | (48H)
Carry
1 1
------------------------------------
1 0 0 1 0 1 1 1 (97H) = 151d
N=1, OV=1, Z=0, DC=1, C=0

## Slide 20: ADDWF Example
Assume we want to add 0x7292 and 0x1F91 REG10=91, REG11=1F
REG20=92, REG21=72
ADDWFC=REG11+REG21+C
0x72+ 0x1F+1= 0x92 (1 0 0 1 0 0 1 0)
N=1, OV=1, Z=0, DC=1, C=1
N=?, OV=?, Z=?, DC=?, C=?
Do 4.5 SE
page 122
REG10+REG20=22 & C=1 (291d)

## Slide 21: Subtraction
Instructions:
 SUBLW
8-bit
 SUBWF
F, d, a
 SUBFWB
F, d, a
 SUBWFB
F, d, a
Examples
 SUBLW 0xA2
Subtract WREG from A2H
 SUBWF REG1, 0
Subtract WREG from REG1 and save the result in W
 SUBWF REG1, 1
Subtract WREG from REG1 and save the result in REG1
 SUBFWB REG2, 0
Subtract REG2, and Borrow from WREG and save the result in W
 SUBWFB REG2, 0
Subtract WREG, and Borrow from REG2 and save the result in W
L-WREG
F-WREG
If the number is larger than 8 bit!

## Slide 22: Example
Assume [W] = 7F and [REG5]=28
SUBWF REG5
Means:28-7FW

## Slide 23: (Adding values larger than 8 bits)
REG10=F2 REG11=29 REG12=87 REG13=35
Write a Program

## Slide 24: Increment, Decrement, and Complement Operations
 DECF
F, d, a
 COMF
F, d, a
 NEGF
F, a
Instructions: Examples:
 INCF F, d, a  INCF REG1,1
Increment REG1 and save result in REG1
DECF REG2, 0 Decrement REG2 and save result in W
COMF REG3,0 Complement REG3 and save result in W
NEGF REG1, 0
Take 2s complement of REG1

## Slide 25: Redirection of Program Execution (Branch and Skip Operations)
 The PIC18F MPU includes three groups of instructions that change the direction of execution:
 Branch
 Skip
 Call (discussed in Chapter 7)

## Slide 26: Branch Instructions in PIC18
Family

## Slide 27: Unconditional Branch Instructions
Instructions:
 BRA
n (label)
 GOTO
k (label)
 Unconditional relative branch within ± 512 words
 Unconditional absolute branch anywhere in 2 MB memory locations

## Slide 28: Conditional Relative
Branch Instructions
 (n is label – represents 8-bit signed number in words)
 BC n: Branch if Carry n is the address the PC should be set to upon |  |  | 
 BNC | n: | Branch if No Carry executing the command! | 
 BZ | n: | Branch if Zero | 
 BNZ | n: | Branch if No Zero For Example: | 
 BN | n: | Branch if Negative BC 0x020 ; goto address 20 BZ LOOP; goto loop | 
 BNN | n: | Branch if No Negative | 
 BOV | n: | Branch if Overflow | 
 BNOV | n: | Branch if No Overflow | 

## Slide 29: Examples of Relative
Conditional Branch Instructions
Correction to the the TEXT:
BC 0x6
This means:
If carry flag is set then jump to 0x06
The n value is where the jump goes to (what the next PC value should be)

## Slide 30: Examples of Relative
Conditional Branch Instructions
BC n refers to the next PC if the condition is met!

## Slide 31: Arithmetic Instructions with Skip
 Compare File (Data) Register with W:
 CPFSEQ | F, a | ;Skip next instruction if F = W
 CPFSGT | F, a | ;Skip next instruction if F > W
 CPFSLT | F, a | ;Skip next instruction if F > W
 Increment File (Data) Register:
 INCFSZ F, d, a
 INFSNZ F, d, a
;Skip next instruction if F = 0
; Skip next instruction if F ≠ 0
 Decrement File (Data) Register:
 DECFSZ F, d, a ; Skip next instruction if F = 0
 DCFSNZ F, d, a ; Skip next instruction if F ≠ 0

## Slide 32: Creating some Delay: Example : When W=0, REG11=1
What is the delay?
Skip next instruction if F = 0 Go to location 0x24

## Slide 33: Creating some Delay: Example : When W=0, REG11=1
Skip next instruction if F = 0 Go to location 0x24
Operand of BRA is the number of words the program should branch;
In this case 1 word backward 
-2=FE; NOTE: D7 is
OPCODE for BRA

## Slide 34: Branch (BRA) Examples
FD = -3; Going back 3 words
Starting with PC=0x28 going to PC=22 That is (28-26) / 2 = 3
FB = -5; Going back 5 words
Starting with PC=0x2A going to PC=20; before the branch is executed the PC=2A That is (2A-20) / 2 = 5
PC+2 + 2*n
28+2 + 2(-5)=2A-A=20

## Slide 35: Branch Example
BAD JUMP!
GOOD JUMP!
GOOD JUMP!
Note that is the program starts at 0x20
And we use BZ 0x2  the jump will to PC=20

## Slide 36: Flowchart for Delay Loop
Delay
Timer
Software
Loops
Nested Loops

## Slide 37: Flowchart for Delay Using Nested Loop

## Slide 38: Nested Loop Delay Analysis




--------------------------------------------- PIC ASSEMBLER LISTING
Line Address Opcode Instruction
---------------------------------------------


;Line removed by MPASMWIN preprocessor:
;Line removed by MPASMWIN preprocessor:
;Line removed by MPASMWIN preprocessor:





COUNT1 REG10 REG11
EQU EQU EQU
Title "Ex5-12 Delay Using Nested Loop" List p=18F452,
#include <p18F452.inc> ;This is a header file for 18F452
D'250' 0x10
0x11

0001 000000
0002 000000
0003 000000
0004 000000
0005 000000
0006 000000
0007 000000
0008 000000
 0009 | 000000 |  |  |  |  | 
 0010 | 000000 | 6A11 |  | CLRF | REG11 | ;Set up REG11= COUNT2 =0 for 256 execution
 0011 | 000002 | 0EFA | LOOP2: | MOVLW | COUNT1 | ;Load decimal count in W
 0012 | 000004 | 6E10 |  | MOVWF | REG10 | ;Set up REG10 as a counter
 0013 | 000006 | 0610 | LOOP1: | DECF | REG10,1 | ;Decrement REG10 - 1W/1C/4CLK
 0014 | 000008 | E1FE |  | BNZ |  | LOOP1 ;Go back to LOOP1 if REG 10 =/ 0
 0015 | 00000A | 0611 |  | DECF | REG11,1 | ;Decrement REG11
 0016 again | 00000C | E1FA |  | BNZ |  | LOOP2 ;Go back to load 250 in REG10 and start LOOP1
 0017 | 00000E |  |  | END |  | 


---------------------------------------------
Number of errors = 0

## Slide 39
 0001 | 000000 ;Line removed by MPASMWIN preprocessor: | Title "Ex5-12 Delay Using Nested Loop"
 0002 | 000000 ;Line removed by MPASMWIN preprocessor: | List p=18F452,
 0003 | 000000 ;Line removed by MPASMWIN preprocessor: | #include <p18F452.inc> ;This is a header file for 18F452
 0004 | 000000 | 
 0005 | 000000 COUNT1 EQU | D'250'
 0006 | 000000 REG10 EQU | 0x10
 0007 | 000000 REG11 EQU | 0x11
 0008 | 000000 | 
 0009 | 000000 | 
 0010 | 000000 6A11 CLRF REG11 | ;Set up REG11= COUNT2 =0 for 256 execution
 0011 | 000002 0EFA LOOP2: MOVLW COUNT1 | ;Load decimal count in W
 0012 | 000004 6E10 MOVWF REG10 | ;Set up REG10 as a counter
 0013 | 000006 0610 LOOP1: DECF REG10,1 | ;Decrement REG10 - 1W/1C/4CLK
 0014 | 000008 E1FE BNZ | LOOP1 ;Go back to LOOP1 if REG 10 =/ 0
 0015 | 00000A 0611 DECF REG11,1 | ;Decrement REG11
 0016 again | 00000C E1FA BNZ | LOOP2 ;Go back to load 250 in REG10 and start LOOP1
 0017 | 00000E END | 


---------------------------------------------
Number of errors = 0
Delay Analysis | DECF1 Cycle; 4 clock periods BNZ 2 Cycles; 8 clock period (w/branch) Iclk=12 clock periods (instruction clock cycles) Tc=1/40MHz=25ns T(one loop)=(1/F ) * Iclk = 12 . 25ns=300 ns Total Delay(N loop)=Count*T=75 us Total Execution time: TL=Iclk*Tc*Nloop
 --------------------------------------------- PIC ASSEMBLER LISTING Line Address Opcode Instruction  --------------------------------------------- | 
Remember: 1W/1C/4Clk  1 Word instruction with one clock cycle with 4 clk periods

## Slide 40
 0001 | 000000 ;Line removed by MPASMWIN preprocessor: | Title "Ex5-12 Delay Using Nested Loop"
 0002 | 000000 ;Line removed by MPASMWIN preprocessor: | List p=18F452,
 0003 | 000000 ;Line removed by MPASMWIN preprocessor: | #include <p18F452.inc> ;This is a header file for 18F452
 0004 | 000000 | 
 0005 | 000000 COUNT1 EQU | D'250'
 0006 | 000000 REG10 EQU | 0x10
 0007 | 000000 REG11 EQU | 0x11
 0008 | 000000 | 
 0009 | 000000 | 
 0010 | 000000 6A11 CLRF REG11 | ;Set up REG11= COUNT2 =0 for 256 execution
 0011 | 000002 0EFA LOOP2: MOVLW COUNT1 | ;Load decimal count in W
 0012 | 000004 6E10 MOVWF REG10 | ;Set up REG10 as a counter
 0013 | 000006 0610 LOOP1: DECF REG10,1 | ;Decrement REG10 - 1W/1C/4CLK
 0014 | 000008 E1FE BNZ | LOOP1 ;Go back to LOOP1 if REG 10 =/ 0
 0015 | 00000A 0611 DECF REG11,1 | ;Decrement REG11
 0016 again | 00000C E1FA BNZ | LOOP2 ;Go back to load 250 in REG10 and start LOOP1
 0017 | 00000E END | 


---------------------------------------------
Number of errors = 0
Delay Analysis | In reality, however: Last loop branches, hence only 8clock cycle Total Actual Execution time: TL=Iclk*Tc*(Nloop-1) + 8*Tc
 --------------------------------------------- PIC ASSEMBLER LISTING Line Address Opcode Instruction  --------------------------------------------- | 
Remember: 1W/1C/4Clk  1 Word instruction with one clock cycle with 4 clk periods

## Slide 41
Line Address Opcode Instruction


---------------------------------------------


;Line removed by MPASMWIN preprocessor:
;Line removed by MPASMWIN preprocessor:
;Line removed by MPASMWIN preprocessor:





COUNT1 REG10 REG11
EQU EQU EQU
Title "Ex5-12 Delay Using Nested Loop" List p=18F452,
#include <p18F452.inc> ;This is a header file for 18F452
D'250' 0x10
0x11

0001 000000
0002 000000
0003 000000
0004 000000
0005 000000
0006 000000
0007 000000
0008 000000
0014 000008 E1FE
BNZ


REG11,1

DECF BNZ
LOOP1 ;Go back to LOOP1 if REG 10 =/ 0
;Decrement REG11
LOOP2 ;Go back to load 250 in REG10 and start LOOP1
0015 00000A 0611
0016 00000C E1FA
again
0017 00000E
END



---------------------------------------------
Number of errors = 0
Nested Loop Delay Analysis | Second Loop: (1/F=25 nsec) 4 Instructions: 4+4+4+8 clock periods=20 Iclk T(loop2)=20*1/F=500 ns T(loop1+loop2)=75+0.5=75.5 us Total Delay=256 * 75.5=19 .328 msec (ignoring the last cycle in each case)
 ---------------------------------------------  PIC ASSEMBLER LISTING | 
 0009 | 000000 |  |  |  |  | 
 0010 | 000000 | 6A11 |  | CLRF | REG11 | ;Set up REG11= COUNT2 =0 for 256 execution
 0011 | 000002 | 0EFA | LOOP2: | MOVLW | COUNT1 | ;Load decimal count in W
 0012 | 000004 | 6E10 |  | MOVWF | REG10 | ;Set up REG10 as a counter
 0013 000006 0610 LOOP1D: elay of abDoEuCtF75 usec REG10,1 |  |  |  |  |  | ;Decrement REG10 - 1W/1C/4CLK

## Slide 42: Calculations for Generating Waveforms
 To generate 50 µS delay, count:
Write a program to generate a square wave of 10KHz freq. by turning Bit0 of PORT C ON & OFF using a 40 MHz clk (25 nsec)
LOOP1:
DECF BNZ
REG10,1 LOOP1
;Decrement REG10 - 1W/1C/4CLK
;Go back to LOOP1 if REG 10 =/ 0
Number of times the program should loop
100 usec
50 usec

## Slide 43: Calculations for Generating Waveforms
Write a program to generate square wave of 10KHz freq. by turning Bit0 of PORT C using a 40 MHz clk (25 nsec)
LOOP1:
BSF
DECF BNZ
PORTB,0
REG10,1 LOOP1
;Decrement REG10 - 1W/1C/4CLK
;Go back to LOOP1 if REG 10 =/ 0
BCF PORTB,0
 To generate 50 µS delay, count:
Number of times the program should loop
100 usec
50 usec

## Slide 44: Generating Waveforms
REG1 EQU REG10 EQU
0x01
0x10
;Address of Data Register1
;Address of Data Register10
START:
ORG MOVLW MOVWF MOVWF
0x20 B'11111110' TRISC REG1
;Load number to set up BIT0 as an output
;Initialize BIT0 as an output pin
;Save Bit pattern in REG1
ONOFF:
MOVFF MOVLW MOVWF
REG1,PORTC D'166'
REG10
;(8 Clk)-Turn on/off BIT0
;(4 Clk) -Load decimal count in W
;(4 Clk) Set up REG10 as a counter
LOOP1:
DECF BNZ
REG10, 1 LOOP1
;(4 Clk) - Decrement REG10
;(8/4 Clk)-Go back to LOOP1 if REG 10 not equal 0
REG1,1 ONOFF
;(4 Clk)-Complement Bit Pattern
;(8 Clk)-Go back to change LED
COMF BRA END

## Slide 45: Delay Recalculations to Account for Outside Instructions – Single Loop

## Slide 46: Adding a Block of Data (P.163)
Add five data bytes stored in data registers
(0x10-0x14). The sum should be displayed at PORTB and PORTC.
Use FSR0 – Pointer
Use a carry register: CYREG
Assume values are given:

## Slide 47: Adding a block of numbers

0x10
0X01
;Define the beginning data register address
;Set up register 01 as a counter
BUFFER COUNTER CYREG
EQU EQU
EQU 0X02
0005 000000
0006 000000
0007 000000
0008 000000
0009 000000
ORG
0x20
;Begin assembly at 0020H
0010 | 000020 0E00 | START: | MOVLW | 0x00 | ;Byte to initialize port as an output port
0011 | 000022 6E93 |  | MOVWF | TRISB | Initialize Ports B &C as an output ports




MOVWF MOVLW MOVWF CLRF LFSR
TRISC 0X05 COUNTER CYREG
FSR0,BUFFER
;Count for five bytes
;Set up counter
;Clear carry register
;Set up FSR0 as pointer for data registers


0012 000024 6E94
0013 000026 0E05
0014 000028 6E01
0015 00002A 6A02
00002C EE00
0016 00002E F010
0017 000030 0E00
NEXTADD:

000032 24EE
0019 000034 E301
MOVLW ADDWF BNC INCF DECF BNZ MOVWF MOVFF
0x00 POSTINC0,W SKIP
CYREG COUNTER,1,0 NEXTADD PORTC
CYREG, PORTB
;Clear W register to save sum
;Add byte and increment FSR0
;Check for carry-if no carry jump to SKIP (branch if C=0)
;If there is carry, increment CYREG
;Next count and save count in register
;If COUNT =/ 0, go back to add next byte
;Display low-order byte of sum at PORTC
;Display high-order byte of sum at PORTB
0020 000036 2A02
0021 000038 0601 SKIP:
0022 00003A E1FB
0023 00003C 6E82
0024 00003E C002
0024 000040 FF81
0025 000042 0003
0026 000044
SLEEP END










---------------------------------------------
Number of errors = 0
How do you modify to make the BUFFER size variable?
Lab:
Assume the total is less than 2FFFF and we can only display two byes Using PORT B and C
Modify the program to calculate the sum of registers 10-19 If the sum is zero set bit 0 of PORTA
If the sum>50H set bit 1 of PORT A

Initialize


Initialize
Ports
Set the Ptr0016
Move the P00t1r8

## Slide 48: Heading and Include files must be included:
Displaying Breakpoints

## Slide 49: Using the Logic Analyzer Problem: 5-23 going to REG3
Results
Directed to PortB
RB0 RB1 RB2 RB3
….
….

## Slide 51: Good Programing

## Slide 52: Example on page 164 – Hide it