## Slide 1: Chapter 9
Input/Output (I/O) Ports and Interfacing
Updated: 3/13/12

## Slide 2: Basic Concepts in I/O Interfacing and PIC18 I/O Ports (1 of 2)
 I/O devices (or peripherals) such as LEDs and keyboards are essential components of the microprocessor-based or microcontroller-based systems.
 Classified into two groups
 input devices
 output devices

## Slide 3: Block Diagram of I/O Interfacing
Access one port at a time 8-bit registers
I/O ports are associated with a SFR Each port is associated with 3 registers:
PORT / LAT / TRIS
Buffer
Latch

## Slide 4: I/O Ports: Interfacing and Addressing
 To read (receive) binary data from an input peripheral
 MPU places the address of an input port on the address bus, enables the input port by asserting the RD signal, and reads data using the data bus.
 To write (send) binary data to an output peripheral
 MPU places the address of an output port on the address bus, places data on data bus, and asserts the WR signal to enable the output port.
 Remember:
 Writing to the port
 When the MPU sends out or transfers data to an output port
 Reading from the port
 When the MPU receives data from an input port

## Slide 5: PIC18F452/4520 I/O Ports (1 of 5)
 MCU includes five I/O ports
 PORTA, PORTB, PORTC, PORTD, and PORTE
 Ports are multiplexed meaning they can be set up by writing instructions to perform various functions
PORTA: Example of Multiple Functions
 Digital I/O: RA6-RA0
 Analog Input: AN0-AN4

V REF+ : A/D Reference Plus
Voltage
 V REF- : A/D Reference
 Minus Voltage
 TOCK1: Timer0 Ext. Clock
 SS: SPI Slave Select Input
 LVDIN: Low voltage Detect Input

## Slide 6: PIC18F452/4520 I/O Ports (2 of 5)
 Each I/O port is associated with the special functions registers (SFRs) to setup various functions.
 Can be set up as entire ports or each pin can be set up.
 PORT: This register functions as a latch or a buffer determined by the logic levels written into the associated TRIS register.
 TRIS: This is a data direction register. Writing logic 0 to a pin sets up the pin as an output pin, and logic 1 sets up the pin as an input pin.
 LAT: This determines if port is bidirectional .

## Slide 7: PIC18F452/4520 I/O Ports (3 of 5)
 Internal block diagram of PORTB includes:
 Three internal D flip-flops (latches)
 Data latch to output data
 TRIS latch to setup data direction
 Input latch for input data

## Slide 8: PIC18F452/4520 I/O Ports (4 of 5)
 PORTB Internal Block Diagram
Three internal D flip-flops (latches):
Data latch to output data TRIS latch to setup data
direction
Input latch for input data
Pull-up
Q- TRIS: 0  A is enabled
Q- TRIS: 1  A is disabled
A

## Slide 9: Interfacing Output Peripherals (1 of 2)
 Commonly used output peripherals in embedded systems are
 LEDs, seven-segment LEDs, and LCDs; the simplest is LED
 Two ways of connecting LEDs to I/O ports:
 LED cathodes are grounded and logic 1 from the I/O port turns on the LEDs - The current is supplied by the I/O port called current sourcing.
 LED anodes are connected to the power supply and logic 0 from the I/ O port turns on the LEDs - The current is received by the chip called current sinking.
Common Cathode
Active high
Common Anode
Active low

## Slide 10: Interfacing Seven-Segment LEDs as an Output (1 of 4)
 Seven-segment LEDs
 Often used to display BCD numbers (1 through
9) and a few alphabets
 A group of eight LEDs physically mounted in the shape of the number eight plus a decimal point as shown in Figure 9-5 (a)
 Each LED is called a segment and labeled as
ʻaʼ through ʻgʼ.

## Slide 11: Interfacing Seven-Segment LEDs as an Output (2 of 4)
 Two types of seven- segment LEDs
 Common anode
 Common cathode
decimal point

## Slide 12: Interfacing Seven-Segment LEDs as an Output (3 of 4)
 In a common anode seven- segment LED
 All anodes are connected together to a power supply and cathodes are connected to data lines
 Logic 0 turns on a segment.
 Example: To display digit 1, all segments except b and c should be off.
 Byte 11111001 = F9H will display digit 1.
5V (Common Anode)

## Slide 13: Interfacing Seven-Segment LEDs as an Output (4 of 4)
 In a common cathode seven-segment LED
 All cathodes are connected together to ground and the anodes are connected to data lines
 Logic 1 turns on a segment.
 Example: To display digit 1, all segments except b and c should be off.
 Byte 00000110 = 06H will display digit 1.
GND (Common Cathode)

## Slide 14: Segment LEDS to PORTB and PORTC

## Slide 15: Seven-Segment Chips
ALPHA/ NUMERIC C/A DISPLAY

## Slide 16: Sample Program

## Slide 17: Interfacing to Multiple 7-Segments

## Slide 18: Using the Simulator

## Slide 19: Interfacing Input Peripherals
 Commonly used input peripherals in embedded systems are:
 DIP switches, push-button keys, keyboards, and A/D converters.
 DIP switch: One side of the switch is tied high (to a power supply through a resistor called a pull-up resistor), and the other side is grounded. The logic level changes when the position is switched.
 Push-button key: The connection is the same as in the DIP switch except that contact is momentary.

## Slide 20: Interfacing Dip Switches and Interfacing LEDs

## Slide 21: Driving an LED
 Transistor inverter acting as the driver
 Assume LED requires 3.5 Volts and 20 mA
 2N2222 is Current Amplifier  generates collector current
(multiplies base-current)
 In this case the current gain is 100!
 Note Vbe=0.7
Q1
2N2222
R1 430
18K
+12V
20 mA
0.2 mA
8.5 V
D1
3.5 V
4.3 V minimum
3.0 mA maximum
Port Pin
8.5 V
20 mA
3.6 V
0.2 mA
4.3-0.7
3.6 V
R2
3.6/18000

## Slide 22: Driving a RELAY & SOLENOID
DS1
25 Watt Lamp
1
2
+5V
LS1 RELAY
SPDT
3
5
4
1
2
R1
5.6K
D1
Q1 2N2222A
RB0
D1
Solenoid
R1
5.6K
 Controlling appliances
 Driving solenoid
+12V
Q1 MPSA13
RB0

## Slide 23: Example: Reading from an I/O Port
 The instruction: MOVF PORTB, W reads from PORTB.
 To execute the instruction, the MPU does the following:
 Reads the instruction from memory
 Places the address of PORTB (F81H) on the address bus of data memory
 Selects PORTB
 Asserts the RD signal and enables PORTB
 Reads logic levels (1/0) of the switches and places on the data bus
 Saves the reading in the WREG

## Slide 24: Internal Pull-Up Resistor (1 of 2)
 The pull-up resistors are connected externally.
However, PORTB can provide equivalent resistors internally through initialization.
 Turning off the internal FET is equivalent to providing a pull-up resistor.

## Slide 25: Internal Pull-Up Resistor (2 of 2)
 Bit7 (RBPU) in the INTCON2 register enables or disables the pull-up resistor
 Instruction to Enable Pull Up Resistors: BCF INTCON2 7, 0
C Code: INTCON2bit.RBPU = 0 // pull-ups on

## Slide 26: Interfacing Push-Button Keys (1 of 2)
 Electrical connection of a push-button key is same as that of a DIP switch except that the connection is temporary when the key is pressed.
 When a key is pressed (or released), mechanical metal contact bounces and can be read as multiple inputs.
 The reading of one contact as multiple inputs can be eliminated by a key-debounce technique, using either hardware or software.

## Slide 27: Interfacing Push-Button Keys (2 of 2)
(a)
(b)

## Slide 28: Various Switches
VCC
VCC
SPDT Pushbutton Switch
SPDT Toggle Switch
10K
DPDT Pushbutton Switch
SPST Toggle Switch
1 2
VCC
10K
VCC
VCC
10K
DPDT Toggle Swtich
10K
10K
SPST Pushbutton Switch
10K
VCC
SPST Toggle Switch
SPST Pushbutton Switch
SPDT Toggle Switch
DPDT Toggle Switch
SPDT Pushbutton Switch
DPDT Pushbutton Switch

## Slide 29: Key Debounce Techniques
 Hardware technique
 Two circuits, based on the principles of generating a delay and switching the logic level at a certain threshold level.
 Two NAND gates connected back to back, equivalent of a S-R latch. The output of the S-R latch is a pulse without a bounce.
 An integrated circuit (MAX 6816) that bounces the key internally and provides a steady output.

## Slide 30: Illustration: Interfacing Push-Button Keys (1 of 6)
 Problem statement
 A bank of push-button keys are connected as inputs to PORTB.
 The pull-up resistors are internal to PORTB.
 Write a program to recognize a key pressed, debounce the key, and identify its location in the key bank with numbers from 0 to 7.

## Slide 31: Interfacing Push-Button Keys (3 of 6)
 Hardware
 PORTB should be set up as input port
 Internal pull-up resistors should be enabled
 Software
 Checking a key closure Debouncing the key
 Encoding the key
Alternatively

## Slide 32: Interfacing Push-Button Keys - Software Debounding
 Checking a key closure
 When a key is open, the logic level is one (assuming pull-ups are enabled) and when it is closed, the logic level is zero.
 When all keys are open, the reading will be 0xFF, and when a key is closed, the reading will be less than 0xFF.
 Therefore, any reading less than FFH indicates a key closure.
 This will be the first read!
 Debouncing the key
 Software technique
 Wait for 20 ms.
 Read the port again.
 If the reading is still less than FFH, it indicates that a key is pressed.
 Encoding the key
 Key closure can be identified by rotating the reading right and looking for ʻNo Carryʼ and counting the rotations

## Slide 33: Software Debouncing – Used for Active LOW!
// >>> Donʼt forget the #include <delays.h> statement <<<
// ************************ Switch *******************************
// to use this function, make sure that it is invoked as follows
//
// Switch( 0x04 )  switch on bit 2
//
// or
//
// Switch( 0x40 )  switch on bit 6
//
// or
//
// Switch( 0x03 )  switches on bits 0 and 1
//
// ********************** CONSTANTS ******************************
// change to match the actual port
// change as needed for time delay – 15 msec.
#define KEYPORT PORTA #define DELAY 15
void Switch( char bit )



















{
   |  | do { | // wait for release while ( ( KEYPORT & bit ) != bit ); | 
  |  | } | Delay1KTCYx(DELAY); | 
 |  |  | while( ( KEYPORT & bit ) != bit ); | 
   |  | do { | // wait for press while ( ( KEYPORT & bit ) == bit ); | 
  |  | } | Delay1KTCYx(DELAY); | 
 | } |  | while( ( KEYPORT & bit ) == bit ); | 
Switch(0x22)
0010 0010
Bits 1 or 5 is activated

## Slide 34: Software Debouncing – Used for Active LOW! Another Example
#define Switch_Pin PORTBbits.RB0 The demo board switch is connected to I/O pin RB0, which is normally pulled up to VDD internally. When the switch is pressed, it pulls RB0 to ground (low state).

## Slide 35: PIC18F46K20 Pin Diagram

## Slide 36: Digital Input Port
Pins are configured as analog or digital in the SFRs ANSEL and ANSELH
PIC18F46K20
Interrupt Control Weak Pull Up
Analog Sel

## Slide 37: Class Exercise
 Find the following bits in the Data Sheet:
 http://ww1.microchip.com/downloads/en/ DeviceDoc/41303G.pdf

## Slide 38: Interfacing a Matrix Keyboard
10K
VCC
1 |  | 2 |  |  | 1 |  | 2 |  |  | 1 |  | 2
 | 1 |  |  |  |  | 2 |  |  |  |  | 3 | 
1 |  | 2 |  |  | 1 |  | 2 |  |  | 1 |  | 2
 | 4 |  |  |  |  | 5 |  |  |  |  | 6 | 
1 |  | 2 |  |  | 1 |  | 2 |  |  | 1 |  | 2
 | 7 |  |  |  |  | 8 |  |  |  |  | 9 | 
1 |  | 2 |  |  | 1 |  | 2 |  |  | 1 |  | 2
 | * |  |  |  |  | 0 |  |  |  |  | # | 
Telephone-style 4x3 Keyboard
Actual Keyboard
Keyboard as seen by software before the lookup table
1 | 2 | 3
4 | 5 | 6
7 | 8 | 9
10 | 0 | 11
0 | 4 | 8
1 | 5 | 9
2 | 6 | 10
3 | 7 | 11
RA0
RA3 RB0
RB2

## Slide 39: Interfacing a Matrix Keyboard
 Software
 To recognize and encode the key pressed, the program should:
 Ground all the columns by sending zeros.
 Check each key in a row for logic zero.
 Ground one column at a time and check all the rows in that column.
 Once a key is identified, it is encoded based on its position in the column.

## Slide 40: Matrix Keyboard Software
//
// key codes for a telephone style keypad
// stored as static constants in the program memory
//
// left column
// middle column
// right column
// set mask
// set number of rows
rom near char lookupKey[] =
{
1, 4, 7, 10,
2, 5, 8, 0,
3, 6, 9, 11
};
//
// uses function Switch
//
unsigned char Key(void)
{
#define MASK 0x0f #define ROWS 4 char a;
char keyCode;
PORTB = keyCode = 0; Switch( MASK ); PORTB = 0xFE;
//clear Port B & keyCode
// de-bounce and wait for any key
// select a leftmost column
while ( ( PORTA & MASK ) == MASK ) // while no key is found
{



























PORTB = (PORTB << 1) | 1;
keyCode += ROWS;
// get next column
// add rows to keycode
// find row
  |  | } for ( a = 1; a != 0; a <<= 1)
 |  | {
  |  | if ( ( PORTA & a ) == 0 ) break;
  |  | keyCode++; }
 |  | return lookupKey[keyCode]; // lookup correct key code
 | } | 
1 | 2 | 3
4 | 5 | 6
7 | 8 | 9
10 | 0 | 11

## Slide 41: 7-Segment Interface
R3 R2 R1 3.9K 10K 10K
C2 30 pF
C1
1.0 uF
C3
0.1 uF
U1
PIC18F1220
1
2
6
7
3
4
16
15
14
5
RA0 RBO
RA1 RB1
RA2 RB2
RA3 RB3
RA4 RB4 #MCLR RB5 OSC1 RB6
OSC2 RB7
VDD
VSS
U2
74LS244
18
16
14
12
20
10
9
7
5
3
19
VCC
GND
A1 A2 A3 A4 A5 A6 A7 A8
Y1 Y2 Y3 Y4 Y5 Y6 Y7 Y8
1OE
2OE
+5V
330
SW1
COUNT
8 | 2
9 | 4
17 | 6
18 | 8
10 | 11
11 | 13
12 | 15
13 | 17
 | 1

## Slide 42
// ***************** program memory data ************************** rom near char look7[] = // 7-segment lookup table
{
active low signals x g f e d c b a
0x40,
0x79,
0x24,
0x30,
0x19,
0x12,
0x02,
0x78,
0x00,
0x10
// 0
// 1
// 2
// 3
// 4
// 5
// 6
// 7
// 8
// 9
};
// ***************** data memory data ***************************** int count;
#pragma code
// *****************de-bounce functions ************************************
// wait for release
void Switch( char bit )
{
do
{
while ( ( PORTA & bit ) != bit ); Delay1KTCYx(30);
// 15 ms delay
}while( ( PORTA & bit ) != bit );
do // wait for press
{
while ( ( PORTA & bit ) == bit ); Delay1KTCYx(30);
}while( ( PORTA & bit ) == bit );
}
// ***************** main program ********************************* void main (void)
{
// Ports A and B are digital
ADCON1 = 0x7F; TRISA = 1;
TRISB = 0;
count = 0;
// Port A, bit 0 is input
// Port B is output
// start count at zero
// main loop
// display number
// wait for pushbutton
while ( 1 )
{
PORTB = look7[count]; Switch( 1 );
count++;
if ( count >= 10 )
count = 0;
}

















































}
7-Segment
Control Software with De-bounce 
Each time the input is
Pressed the number Shown by the 7-segemnt Increments!

## Slide 43: Interfacing LCD (Liquid Crystal Display)
 Problem statement
 Interface a 2-line x 20 character LCD module with the built-in HD44780 controller to I/O ports of the PIC18 microcontroller
 Multi-LCDs refer to LCDs with different interfaces

## Slide 44: Converting to ASCII
 The LCD can represent characters in ASCII
 For example number 0x08  must be converted to 0x38
 To perform this:
 If W=0x08 then ASCII=XORLW 0x30W=38

## Slide 45: Interfacing LCD
 Hardware
 20 x 2-line LCD displays (two lines with 20 characters per line)
 LCD has a display Data RAM (registers) that stores data in 8-bit character code.
 Each register in Data RAM has its own address that corresponds to its position on the line.
 The address range for Line 1 is 00 to 13H and Line 2 is 40H to 53H.
PICDEMO
0x38
0x39
0x00
2x20
0x38
0x013
0x014
0x040
0x053
8
8

## Slide 46: Interfacing LCD
 Driver HD77480
 Three control signals:
 RS – Register Select (RA3)
 R/W – Read/Write (RA2)
 E – Enable (RA1)
 Three power connections
 Power, ground, and the variable register to control the brightness

## Slide 47: Interfacing LCD
 Can be interfaced either in the 8-bit mode or the 4-bit mode
 In the 8-bit mode, all eight data lines are connected for data transfer
 In the 4-bit mode, only four data lines (DB7-DB4 or DB3-DB0) are connected and two transfers per character (or instruction) are needed
 Driver (HD77480) has two 8-bit internal registers
 Instruction Register (IR) to write instructions to set up LCD
 Data Register (DR) to write data (ASCII characters)
IR REGISTER
DR REGISTER

## Slide 48: Command and Instruction set for LCD type HD44780

## Slide 49: Interfacing LCD
 LCD Operation
 When the MPU writes an instruction to IR or data to DR, the controller:
 Sets the data line DB7 high as a flag indicating that the controller is busy completing the operation
 Sets the data line DB7 low after the completion of the operation
 The MPU should always check whether DB7 is low before sending an instruction or a data byte
 After the power up, DB7 cannot be checked for the first two initialization instructions.

## Slide 50: Interfacing LCD
 Writing to or reading from LCD
 The MPU:
 Asserts RS low to select IR
 Reads from LCD by asserting the R/W signal high
 Asserts the E signal high and then low (toggles) to latch a data byte or an instruction
 Asserts RS high to select DR
 Writes into LCD by asserting the R/W signal low
 Asserts the E signal high and then low (toggles) to latch a data byte or an instruction

## Slide 51: HD44780 Bus Timing
Read timing diagram
Write timing diagram
Asserts RS high to select DR
Writes into LCD by asserting the R/W signal low
Asserts the E signal high and
then low (toggles) to latch a data byte or an instruction
RS is asserted High

## Slide 52: Interfacing LCD (Write)
 Software
 To write into the LCD, the program should:
 Send the initial instructions (commands) before it can check DB7 to set up the LCD in the 4-bit or the 8-bit mode.
 Check DB7 and continue to check until it goes low.
 Write instructions to IR to set up the LCD parameters such as the number of display lines and cursor status.
 Write data to display a message.

## Slide 53: Resetting LCD
 In 4-bit mode the data is sent in nibbles
 First we send the higher nibble and then the lower nibble.
 To enable the 4-bit mode of LCD, we need to follow special sequence of initialization that tells the LCD controller that user has selected 4-bit mode of operation:
 Wait for about 20mS
 Send the first init value (0x30)
 Wait for about 10mS
 Send second init value (0x30)
 Wait for about 1mS
 Send third init value (0x30)
 Wait for 1mS
 Select bus width (0x30 - for 8-bit and 0x20 for 4-bit
 Wait for 1mS
http://www.8051projects.net/lcd-interfacing/commands.php

## Slide 54
http://www.youtube.com/watch?v=tTym5apZwCE
http://video.google.com/videoplay?docid=7437543675646211278#

## Slide 55: Organic LED
 Organic light-emitting diodes - OLEDs - emit light when a current flows through them
 Unlike conventional LEDs, OLEDs are made from layers of plastic and other organic (carbon-based) materials
 Very flexible!
 Applications: displays in MP3 players and phones
 Advantages:
 cheaper than the techniques required to make conventional LEDs.
 inherently thin
 can be made on flexible plastic substrates
 all colors, and multi-colors, are possible
 Disadvantages
 incredibly sensitive to moisture which leads to short life - glass blocks
all moisture, so displays made on a glass substrate and covered by a second glass sheet can have a long life, particularly if the edges are hermetically sealed
http://en.wikipedia.org/wiki/Organic_LED

## Slide 56: Organic LED
 OLEDs are generally made of several layers
 A typical stack (variations are possible):
 Anode
 Electron donor
 Electron transport
 Emitter
 Hole transport
 Hole donor.
 Cathode

## Slide 57: References
http://home.iae.nl/users/pouweha/lcd/ lcd0.shtml
Huang