## Slide 1: Introduction to SPI and I2C
Dr. Farid Farahmand

## Slide 2: PIC Serial Interface

## Slide 3: PIC Out for MSSP (Master Synchronous Serial Port)

## Slide 4: MSSP Module -­‐ SPI
Supports SPI and I2C Protocols
SPI: Serial Peripheral Interface
  Applications: Interface to EEPROM, ADC, Sensors, LCD
  Characteristics: Slower than parallel port, fewer signals
SPI General Operation:
  4-­‐ Wire communication (clock, data in, data out, CS)
  Synchronous  high speed interfaces can be handled
  Master/Slave conﬁguration – the master chip controls all the slaves and provided clock
  Uses serial data exchange protocols (MSB goes out ﬁrst)
  Data exchange can be on rising or falling edge of the clock

## Slide 5
SPI Protocol Interface
RC5=
RC4=
RC3=
Write/Read Characters into SSPBUFF

## Slide 6: SPI Protocol Interface
RC5=
RC4=
RC3=
Data is being broadcasted to all chips

## Slide 7: SPI Application Example
Registers: SSPCON1 SSPSTAT TRISC

## Slide 8: SPI Programing Example
g edge of the clock
Assume:
  Fosc = 10 MHz;
  Data Transfer is 2.5 MHz
  Data is sampled at the fallin
  Data sent at the rising edge of the clock
  Idle clock state is HIGH
What will be the conﬁguration for the Master and Slave Chips
Write the code to transmit characters

## Slide 9: SPI Programing Example (solution)
Master Mode
SSPCON1 Register
Set to SPI Mater Mode Fosc/4 = 2.5 MHz
SSPCON1 bit.CKP = 1
SSPCON1 bit.EN = 1
–  SSPCON1 = 0011 0000
SSPSTAT Register
SSPSTAT bit.SMP = 0 ; rising edge; idle is high
SSPSTAT bit.CKE = 1
SSPSTAT bit.BF = 0
–  SSPSTAT = 0100 0000
TRISC Register
TRISCbit.SDO (RC5) = 0
TRISCbit.SDI (RC4) = 1
TRISCbit.SCK (RC3) = 0
TRISCbit.SS (RC0) = 0
–  TRSC = 0001 0000

## Slide 10: SPI Programing Example (solution) Slave Mode
SSPCON1 Register
–  SSPCON1 = 0011 0100
SSPSTAT Register (same)
–  SSPSTAT = 0100 0000
TRISC Register
TRISCbit.SDO (RC5) = 0
TRISCbit.SDI (RC4) = 1
TRISCbit.SCK (RC3) = 1
TRISCbit.SS (RC0) = 1
–  TRSC = 0001 1001
Timing Diagram

## Slide 11: SPI Programing Example (solution) Master Mode Program
Setup TRISC, SSPCON1, & SSPSTAT
Set ChiSel=0
Write a charcter (0x55) into SSPBUF
Loop: Check if SSPBUF.bit.BF = 1 (buﬀer is full)
IF so : MOVF SSPBUFWREG
Set ChipSel = 1 (deactivate the slave chip)
Timing Diagram

## Slide 12: Inter-­‐Integrated Circuit (I2C) Interface
Created by Philips Inc
Designed to interface ICs on PCB boards (I2C)
Characteristics:
  2-­‐Wire (SCK & SDA)
  Synchronous (100 Kbs or 400 Kbps)
  Master/Slave modes of operation
  Addressing can be 7 or 10 bit

## Slide 13: Pin Out for MSSP I2C Interface

## Slide 14: I2C Interface
2-­‐ Wire Interface
Registers: SSPCON1 SSPSTAT TRISC
SSPCON2 (port idle or not) SSPADD (address)
SSPSR
SSPBUF (data read/write)

## Slide 15: I2C Programing Example
Assume:
  Fosc = 10 MHz;
  I2C Master Mode
  Transmission Rate is 100 KHz
  Enable slew rate for high speed
  No error detection
What will be the conﬁguration for the Master
Write the code to transmit characters

## Slide 16: I2C Programing Example (solution)
Master Mode
SSPCON1 Register
Set to SPI Mater Mode Fosc/4 = 2.5 MHz
SSPCON1 bit.CKP = 1
SSPCON1 bit.EN = 1
–  SSPCON1 = 0011 0000
SSPSTAT Register
SSPSTAT bit.SMP = 0 ; rising edge; idle is high
SSPSTAT bit.CKE = 1
SSPSTAT bit.BF = 0
–  SSPSTAT = 0100 0000
TRISC Register
TRISCbit.SDO (RC5) = 0
TRISCbit.SDI (RC4) = 1
TRISCbit.SCK (RC3) = 0
TRISCbit.SS (RC0) = 0
–  TRSC = 0001 0000

## Slide 17: Programing Example
WREG=
Character
Is I2C
Idle
Is TX in progress
WREG=
Character
Is FLAG
cleared
W = SSCON2
If bit0-­‐bit 4 of SSPCON2 = 1  not in idle mode Else: Check SSPSTATbit.RW; If 1  Transmit
W = Character MOVWF SSPBUF
Check SSPSTATbit.BF = 0
Go to next Character Transmission