## Slide 1
Clocks, Watchdog Timer / Timers

## Slide 2: Reset Conditions
Master Clear
Initializes the MCU Starts with memory 0x00
RC time constant 10-20 msec (R=10K/C=1uF)
#pragma config MCLRE = ON
R1 R
VCC
C1 C
MCLR SW

## Slide 3: Watchdog Timer
The watchdog timer is a device that resets the microcontroller if it is allowed to expire.
The watchdog timer is programmable to expire between 4 ms and 131 seconds.
The watchdog timer is restarted with a ClrWdt() function in C-Language to reset it so it does not expire and cause a reset.
C statement | Assembly Language | Scaling factor | Time to Reset
#pragma config WDTPS = 1 | _WDTPS_1_2H | 1:1 | 4 ms
#pragma config WDTPS = 32768 | _WDTPS_32768_2H | 1:32768 | 131.072 sec

## Slide 4: Brownout Reset
The brownout reset is programmed and used to reset the microcontroller if the power supply voltage drops below a pre-programmed value.
The brownout reset triggers the microcontroller and waits at the reset state until the power supply voltage returns to a level higher then the programmed brownout voltage.
C language | Assembly Language | Brownout Voltage
#pragma config BORV = 45 | _BORV_45_2L | 4.5 V
#pragma config BORV = 42 | _BORV_42_2L | 4.2 V
#pragma config BORV = 27 | _BORV_27_2L | 2.7 V
#pragma config BORV = 20 | _BORV_20_2L | 2.0 V

## Slide 5: Clocks
The PIC18 family allows many different clocking modes for operation. Some include internal timing and some external.
External timing sources are very accurate and are crystal- or resonator-based. A less accurate, but less expensive timing source is an RC circuit. An oscillator module or external timing signal can also be used for the microcontroller.

## Slide 6: Clock Sources
1. Low power crystal (LP)
2. Crystal or ceramic resonator (XT)










*some versions do not have an internal oscillator and
some versions may have additional modes
Examples of
External XTL or ceramic
High-speed crystal or ceramic resonator (HS) Resonator (OSC1/OSC2)
High-speed crystal or ceramic resonator with PLL (HSPLL)
External resister/capacitor with Fosc/4 output on OSC2 (RC)
External resister/capacitor with I/O on OSC2 (RCIO)
*Internal oscillator with Fosc/4 on RA6 and I/O on RA7 (INTIO1)
*Internal oscillator with I/O on RA6 and RA7 (INTIO2)
External clock with Fosc/4 (EC)
External clock with I/O on RA6 (ECIO)

## Slide 7: MCU Clock Source Diagram

## Slide 8: XTL / Ceramic Clock Source Connection
PIC
OSC1
OSC2
PLL internal function Allows multiplying the External clock by 4;
This is used to reduce the EMI (Electromagnetic Interference) on the board

## Slide 9: RC Oscillator Clock Source Connection
OSC2 Fosc/4 OSC1
PIC
External Clock Input
OSC1
External clock source Connected to OSC1
External resister/capacitor with Fosc/4 output on OSC2 (RC) 2 MHz operation is attained with R = 3.9K
and C = 30 pF, Fosc/4 is 500 KHz with these values Frequency = 1/[RC(4.2)] ; can vary slightly

## Slide 10: Clock Examples
#pragma config OSC = HS // high speed crystal oscillator
#pragma config OSC = RC // RC oscillator
#pragma config OSC = INTIO1 // internal oscillator
OSCCON Register

## Slide 11: Programming Example
#pragma config MCLRE = ON #pragma config OSC = HS #pragma config WDT = ON #pragma config WDTPS = 256 #pragma config BORV = 42 #pragma BOR = ON
// enable master clear input
// select crystal oscillator
// set watchdog
// watchdog time is 1 second
// set brownout reset voltage
// brownout is on
void main(void)
// initialize system here
while ( 1 )
{
ClrWdt();
// main program loop
// reset watchdog
// system software goes here
}

## Slide 12: Basic Concepts in Counters and Timers
In digital systems
  Counting is a fundamental concept.
  Clock is an essential element.
  Count is in synchronization with the clock.
  Count is converted in time by multiplying the count and the clock period.

## Slide 13: Hardware Counters and Timers
Counter is a register that can be loaded with a binary number (count) which can be decremented or incremented per clock cycle.
Calculating time:
  Find the difference between the beginning count and the last count
  Multiply the count difference by the clock period
The register can also be used as a counter by replacing the clock with a signal from an event.
When a signal from an event arrives, the count in the register is incremented (or decremented); thus, the total number of events can be counted.

## Slide 14: Types of Counters
Up-counter
  Counter is incremented at every clock cycle
  When count reaches the maximum count, a flag is set
  Counter can be reset to zero or to the initial value
Down-counter
  Counter is decremented at every clock cycle
  When count reaches zero, a flag is set
  Counter can be reset to the maximum or the initial value
Free-running counter
  Counter runs continuously and only readable
  When it reaches the maximum count, a flag is set
What are applications on timers?

## Slide 15: Timer Applications
Time delay
Pulse wave generation
Pulse width or frequency measurement
Timer as an event counter

## Slide 16: Capture, Compare, and PWM (CCP) Modules
CCP modules are commonly found in recent microcontrollers
  16-bit (or two 8-bit) registers specially designed to perform the following functions in conjunction with timers
    Capture: The CCP pin can be set as an input to record the arrival time of a pulse.
    Compare: The CCP pin is set as an output, and at a given count, it can be driven low, high, or toggled.
    Pulse width modulation (PWM): The CCP pin is set as an output and the duty cycle of a pulse can be varied.
      The count for the period and the duty cycle are loaded into CCP registers.
      In this mode, the duty cycle of the output pulse can be varied.

## Slide 17
Same for:

## Slide 18: PIC18 Timers
The PIC18 microcontroller have multiple timers, and all of them are up-counters.
Timers are divided into two groups: 8-bit and 16-bit
Labeled as Timer0 to Timer3 or Timer4 (if available)
  Timer0 can be set up as an 8-bit or 16-bit timer.
  Timer1 and Timer3 are 16-bit timers.
  Timer2 and Timer4 (if available) are 8-bit timers.
Each timer associated with its Special Function Register (SFR): T0CON-T3CON or T4CON

## Slide 19: Timer0
Timer0 8- bit
Timer0 16-bit
Timer0 Control Register (T0CON)
Can be set up as an 8-bit or 16-bit timer
Has eight options of pre-scale values (Divides)
Can run on internal clock source (instruction
cycle) or external clock connected to pin RA4/T0CK1
Generates an interrupt or sets a flag when it
overflows from FFH to 00 in the 8-bit mode and from FFFFH to 0000 in the 16-bit mode
Can be set up on either rising edge or falling edge when an external clock is used
Instruction cycle = 4 clock cycle
Note: TMR Flags are set when the counter reg. has reached it max.

## Slide 20: Timer0
Timer0 8- bit
Timer0 16-bit
Timer0 Control Register (T0CON)
Can be set up as an 8-bit or 16-bit timer
Has eight options of pre-scale values (Divides)
Can run on internal clock source (instruction
cycle) or external clock connected to pin RA4/T0CK1
Generates an interrupt or sets a flag when it
overflows from FFH to 00 in the 8-bit mode and from FFFFH to 0000 in the 16-bit mode
Can be set up on either rising edge or falling edge when an external clock is used
Instruction cycle = 4 clock cycle

## Slide 21: TIMER0 Registers

## Slide 22: Timer0
TMROH buffer between internal data bus and TMR0 high byte
  Read from the TMR0L register, the upper half of Timer0 is latched into the TMR0H register
  Ensures that the PIC18 always reads a 16-bit value that its upper byte and lower byte belong to the same time (since only read 8-bits at a time)

## Slide 23: Timer0 Control Register (1 of 2)
 Timer0 as timer


Bit5 must be cleared to use the internal clock.
At each instruction cycle (four clock cycles), the timer register is incremented.
 Timer0 as a counter



Bit5 must be set 1 to use an external clock.
In this mode, input signal at PORTA-pin RA4/T0CK used as a clock.
When Bit4 = 1, register is incremented on the falling edge, and when Bit4 = 0, the register is incremented on the rising edge.
 Prescaler


Divides clock frequency by a specified ratio.
To use prescaler, Bit3 = 0, and three bits Bit2-Bit0 specify scaler ratio from 1:2 to 1:256

## Slide 24: Timer0 Control Register (2 of 2)
Interrupt
  When Timer0 overflows from FFH to 00 in the 8-bit mode and from FFFFH to 0000 in the16-bit mode, it sets TMR0IF (Timer0 Interrupt Flag) –Bit2 in the INTCON register.


Flag can be used two ways: 1) a software loop can be set up to monitor the flag, or 2) an interrupt can be generated.
Flag must be cleared to start the timer again.
16-bit mode
  When Timer0 is set in the 16-bit mode, it uses two 8-bit registers TMR0L and TMR0H.

## Slide 25: Control Word to Initialize Timer0

## Slide 26: Example - Set TMR0 as an 8-bit timer
Every instruction cycle the register is updated  4x(Clock_Period)
With a pre-scale=1:256 (divide the clock by 256) pre_scalex4x(Clock_Period)
8-bit register allows counting 256 values 
  (2^n)x pre_scalex4x(Clock_Period)
Assuming using a 10MHz internal clock, rising edge clock, how often the flag is set if timer 0 is set as 8-bit counter? What should TMR0 (T0CON ) setup be?
256x256x4x0.1E-6=Every 26.21 msec
1
1
0
0
0
1
1
1

## Slide 27: Timer1 – 16-bit (1 of 5)
A 16-bit counter/timer with two 8-bit registers (TMR1H and TMR1L); both registers are readable and writable
Four options of prescale value (Bit5-Bit4)
Clock source (Bit1) can be internal (instruction cycle) or external (pin RC0/T13CK1) on rising edge
Sets flag or generates an interrupt when it overflows from FFFFH to 0000
Used to synch with the rising edge of the external clock

## Slide 28: Timer1 (3 of 5)
Timer1 Operation
  Can operate in three modes:
    timer,
    synchronous counter,
    asynchronous counter
  Bit0 enables or disables the timer
  When Bit1 = 0, it operates as a timer and increments count at every instruction cycle.
    When Bit1 = 1, it operates as a counter and increments count at every rising edge of the external clock.
  When Bit3 = 1, Timer1 oscillator is enabled which is used for low frequency operations.

## Slide 29: Timer2
Two 8-bit registers (TMR2 and PR2)
An 8-bit number is loaded in PR2 and the timer is turned on, which is incremented every instruction cycle.
When the count in the timer register and the PR register match, an output pulse is generated and the timer register is set to zero.
The output pulse goes through a postscaler that divides the frequency by the scale factor and sets the flag TMR2IF-
Bit1 in the Peripheral Interrupt Register1 (PIR1) that can be used to generate an interrupt.
Pulse
Master Synchronous Serial Port (MSSP)
Freq. Clk

## Slide 30: Example for Timer2
 Generate a periodic high-priority interrupt every 8-msec using Timer2. Assume a 32-MHz crystal oscillator.
Assume post/pre scaled values are 16
Loaded value in PR2 will be


PR2 = [Td / [Inst. Clock Cycle(4) x Prescaler x PostScaler x clock period)]] - 1 PR2 = [ 8msec/[4x16x16x(1/32MHZ)] ] -1 =249
TMR2
Comp
PR2
PR2=249 RCON: IPEN=1
IPR1: TMR21P=1; TMR2IF=CLR INTCON=C0; GLOBAL INT
T2CON=7E; TMR2 ENABLE AND SCALING SETUP PIE1: TMR2IE=SET
Remember, we start
with 0 count  -1 is needed

## Slide 31: Example for Timer2 - continue
 Actual code:
PR2=249 RCON: IPEN=1
IPR1: TMR21P=1; TMR2IF=CLR INTCON=C0; GLOBAL INT
T2CON=7E; TMR2 ENABLE AND SCALING SETUP PIE1: TMR2IE=SET

## Slide 32: Timer3
 Similar to Timer1

## Slide 33: Timer4
Only available to the PIC18F8X2X and PIC6X2X devices
The value of TMR4 is compared to PR4 in each clock cycle
When the value of TMR4 equals that of PR4, TMR4 is reset to 0
The contents of T4CON are identical to those of T2CON
….similar to Timer2 (Two 8-bit registers )