## Slide 1: Introduction UART

## Slide 2: Communication Protocols
Parallel Vs. Serial
  Parallel: Faster / More expensive
  Serial: Cheaper / slower

## Slide 3: Communication Protocols
Timing in serial communication
  Synchronous Serial
  Asynchronous Serial
Rules of Asynch. Protocols
  Synch bit
  Parity bit
  Baud rate
  Data bit

## Slide 4: Parity and Baud Rate
Parity
– Even Parity : 10101010101  6 one’s  EP=0
– Odd Parity : 01010101010  5 one’s  OP=0
Baud Rate
  Pulse per second
  In digital world: Bits per second
  9600 baud  9600 bps or 104 µs per bit.
Synch bit
Required to define the beginning/end of the data
the start bit [LOW] and the stop bit [HIGH]
9600 8N1 – 9600 bps/
8 bits per data / No parity / One Stop bit Always has start bit

## Slide 5: Questions
What will be the EVEN parity value if n=1111 1110?
What will be the ODD parity value if n=1111 1110?
How long does it take to transmit a 1-Mbit file at 9600 baud rate?
Let’s say P represents Even Parity. Assume P=1. Can we accept this as a correct frame: 1101 1110P?

## Slide 6: Serial Communication
Universal Asynchronous Receiver and Transmitter (UART)
  UART is programmable.
  Asynchronous
  Sender provides no clock signal to receivers
  FT232R converts the UART port to a standard USB interface

## Slide 7: Data Frame
7
Data frame
– One start bit
– Data (LSB first or MSB, and size of 7, 8, 9 bits)
Optional parity bit
One or two stop bit
Tolerate 10% clock shift during transmission
Sender and receiver uses the same transmission speed
Overhead % =
1 - (Useful Data / Total Data)
9600/(1 + 8 + 1 + 1) = ~872 frames/second

## Slide 8: Problem
Assume we have a file with size 1 million bits. Assume we use 9600:8-1-1 (includes STOP and SATRT bits). How long does it take to transmit the file? Calculate the Overhead %.
  8-1-1 each frame has 11 bits
  Baud rate is 9600 bits/sec--> Frame rate = 9600/11=872.72 Frames/sec or 1.146 msec/frame
  Number of frames generated: 1,000,000 bits x 1 frame/8 bit= 125,000 frames
  Time to transmit 125,000 frames = 125000 frame x 1.146 msec/frame = 143.25 sec!
  Overhead % = [1 - (Useful Data / Total Data)]x100 = [1 - (8/11)] x 100=27.3
How long does it take to transmit 100,000 bits at 57,600 baud rate?

## Slide 9: Communication Modes
A serial interface can have different communication modes
  Full Duplex - means both devices can send and receive simultaneously.
  Half-Duplex - means serial devices must take turns sending and receiving.

## Slide 10: Differential Vs. Single Ended
Signal with less noise!

## Slide 11: UART Protocols Different Voltage Levels
Standard | Voltage signal | Max distance | Max speed | Number of devices supported per port
RS-232 | Single end ( logic 1: +5 to +15V, logic 0: -5 to -15 V) | 100 feet | 115Kbit/s | 1 master, 1 receiver
RS-422 | Differential (-6V to +6V) | 4000 feet | 10Mbit/s | 1 master, 10 receivers
RS-485 | Differential (-7V to +12V) | 4000 feet | 10Mbit/s | 32 masters, 32 receivers

## Slide 12: Interfacing
Note that in general we SHOULD use something like Maxim's MAX232 in order to ensure voltage compa)bility between the PIC and the RS232 or the terminal
It is also possible to INVERT polarity of the signals on TX and RX pins of USART, to interface to the terminal

## Slide 13: UART Connection
19
To send and receive data using UART we can use several methods including:
polling, interrupt
PIC
PIC
PIC